## Slide 1: Op-amp Design (expt.5)
Design and simulate in PSPICE, an operational amplifier circuit.
The four ‘building blocks’ are:
  differential input stage (long-tailed pair)
  common emitter amplifier
  emitter follower
  current mirror circuit
Briefly investigate each of these circuits in turn before combining them to produce the operational amplifier circuit to a given specification.
These slides are on VITAL under ‘Assignments’

## Slide 2: Specification
Differential input impedance, Rid > 100kΩ
Voltage gain (Aol) greater than 500,000
Output impedance, Ro < 1kΩ
Output voltage to be ‘zero’ volts for zero input
Frequency response down to D.C.
Supply voltage +9 to -9 V
total current consumption not greater than 5mA

## Slide 3: DC characteristics [see ‘Part 2’ slides on VITAL]
IB
IC
VCE
Common-emitter, DC current gain
Common-emitter, AC current gain
Note: different notation
Q: How could we estimate AC gain from DC characteristics?
b
c
e

## Slide 4: Pre-lab
Learn how to design the ‘building blocks’
Part 2 Notes
EF and CE stages
Part 4 Notes
Simple CM
Part 4 Notes
Widlar CM
Part 3 notes
Differential Amp
Part 5 Notes
Active loads
Part 2 Notes
Simple CM

## Slide 5: Putting it together...
Differential Amplifier
Emitter Follower
Common
Emitter
Vout
May need another block to meet the spec on ROUT....
VEE
VCC
Use an active load here, not a resistor or you won’t get enough gain
VEE
VCC
A CC stage to match the input and CE voltage gain stages
VEE
VCC
Always check the dc levels (voltages, currents) first
Remember loading effects of one stage on another

## Slide 6: CE amp with CM load
Can use this to check the gain once you have it biased correctly
Set IC to your desired value
Choose Ibias to set Vout = 0V
(use a dc sweep of Ibias as before)
VCC = 9V, VEE = -9V
What is the V-drop across the resistor?
What value will give 1mA?
R
VCC
VEE

## Slide 7: Output resistance of a CE amp with CM load
VCC = 9V, VEE = -9V
What is the V-drop across the resistor?
What value will give 1mA?
R
VCC
VEE
You can find the Early voltage from the model listing for the transistor
Same analysis applies for the Diff Amp output
If the CE is connected to a load (another stage), it’s ac load is

## Slide 8: Matching the Diff Amp to the CE
V?
I?
RE effectively acts as a current source (with VEE)
RE
Ac load for Diff. amp. is

## Slide 9: The VTC is a handy way to estimate gain
First, look at the Voltage Transfer Curve (VTC) of an amplifier.
Attach the negative input to ground)
Sweep the voltage on the positive input

## Slide 10: Or: alternative way to measure Aol
Measuring the very high Aol is problematic as the amplifier is unstable.
A method for measuring Aol is shown below.
Exercise: Prove the equation by equating currents between vY and ground
vi
+
+
-
vo
10k
10k
10k
100R
vY

## Slide 11: Hints for calculations (VITAL, ‘Assignments’)

## Slide 12: Some advice
Study the script and think about the design beforehand..
Use your ELEC271 notes!
Bring your record of the pre-lab questions to the laboratory – needed when designing the complete OPAMP circuit.
Always check dc levels FIRST!! – check they are as expected
Remember loading effects of one stage on another (Part 2 notes)
Ask questions
Good luck